## Slide 1: Systems Analysis
ROBOCOP – Team Delta
Christine Brennan
  Systems Engineering Process Team Lead
  Based out of TARDEC in Warren, MI
Bill Berklich
  Architecture and Logical Design Lead
  Based out of TARDEC in Warren, MI
Steve Mazza
  Requirements Lead
  Based out of CERDEC in APG, MD
Michael Oexmann
  Systems Integration Lead
  Based out of CERDEC in APG, MD
Ralph Pinnock
  Reliability, Availability, Maintainability – Test (RAM-T) Lead
  Based out of TARDEC in Warren, MI
Dan Torres
  Risk and Technical Planning Lead
  Based out of TARDEC in Warren, MI
US FOB
“Our Mission is to ensure you complete yours”

## Slide 2: Table of Contents
Cost Estimates per Variant
Life cycle cost differences
Variant Value Score
Value Curves
OMOE vs cost Evaluation
Preferred Concept Alternative
SV-7
SV-9
System Baseline
Summary of Results
Appendix A - System/subsystem specification (Type A)
Appendix B – Test program plan outline
2

## Slide 3
Expensive
Moderately Expensive
Affordable
Cost Estimate Per Variant
Detection System | Assessment System | Communication System | Defense System
Passive Infrared Detector | Blue Force Tracker | Computer | CROWS
Radar | Biometric Scanner | Siren | Semi Autonomous Armed UGV
Semi Autonomous UMS | Computer SW | Intrabase Network | Deployable Tire Spikes
 | IR/Thermal/NV Imaging |  | 
 | Threat Prioritization Matrix SW |  | 
Radar | Blue Force Tracker | Siren | Semi-Autonomous Armed UGV
Infrared Camera | IR/Thermal/NV Imaging | Intrabase Network | Deployable Tire Spikes
Camcorder | Vector Analysis | Server System | 
 | Video |  | 
 | Threat Prioritization Matrix SW |  | 
Microphone | IR/Thermal/NV Imaging | Radio | Semi-Autonomous Armed UGV
Boomerang | Biometric Scanner | Lights | Deployable Tire Spikes
Radar | Computer SW | Computer System | 
 | Threat Prioritization Matrix SW |  | 
Inertia Sensor | Ground Sensor | Satellite | Semi – Autonomous Weapon
Microphonic System | Sonic Signature | Phone | Deployable Tire Spikes
Unmanned Aerial Vehicle (UAV) | Computer SW | Computer | 
 | Response Matrix SW |  | 
Notes: Bill Berklich – Explanation of colors, process, findings ect.

## Slide 4: Cost Estimate Per Variant (Con’t)
1 | 1 | 2 | 1 | 3 | 6.38
 | 2 | 2 | 1 | 3 | 
 | 3 | 1 | 3 | 1 | 
 | 0 | 2 | 0 | 0 | 
 | 0 | 1 | 0 | 0 | 
2 | 2 | 2 | 1 | 3 | 5.25
 | 1 | 2 | 3 | 1 | 
 | 1 | 1 | 2 | 0 | 
 | 0 | 1 | 0 | 0 | 
 | 0 | 1 | 0 | 0 | 
3 | 1 | 2 | 1 | 3 | 4.81
 | 2 | 2 | 1 | 1 | 
 | 2 | 1 | 2 | 0 | 
 | 0 | 1 | 0 | 0 | 
4 | 1 | 2 | 3 | 3 | 5.06
 | 2 | 2 | 1 | 1 | 
 | 3 | 1 | 1 | 0 | 
 | 0 | 2 | 0 | 0 | 
A general estimate of cost for each variant using a roll-up method whereby each of the subsystems was assigned a color for the relative figure-of-merit cost. Red was assigned to those systems deemed to be expensive either based on existing cost, estimated component cost or cost of potential development. Yellow was assigned to systems that are close to fielding or have been fielded and have high lifecycle costs. Green was assigned to existing, low-tech solutions that have had extensive use in the field and because of generally low cost are ubiquitous, easy to procure and easy to support, that is they have a low lifecycle cost.
The process of determination of the relative figure of merit consisted of breaking down and categorizing the types of subsystems within each of the proposed options. Then SMEs, SEs and acquisition experts were consulted regarding relative cost. These relative rankings were averaged binned to reach the R/Y/G rank.
Based on the relative cost rank of the systems option #3 is the best cost solution using a series of low-tech and midrange subsystems.

## Slide 5: Life cycle cost differences
Technologies have been assessed and estimated for procurement, development and life cycle cost:
Concept 1:
Unmanned Aerial Vehicles, semi autonomous weapons, and unmanned ground vehicles all have relatively high up front development costs and high
operating costs. (Power budgets may also be a concern for the smaller FOBs, where no power infrastructure is available to integrate with.)
In addition UMS have a relatively low reliability and more expensive specialized components for replacement which will ultimately drive up the cost of
the O&S.
Radar’s reasonable procurement system cost is somewhat offset by higher operational costs due to very high power consumption (again possibly a
feasibility criteria for use on smaller FOBs due to power budget)
Intrabase network costs are expected to be very high for procurement, as a variety of interconnections and associated hardware components may be
required to link previously disconnected local area FOBs and camp outposts
Concept 2:
Radar’s reasonable procurement system cost is somewhat offset by higher operational costs due to very high power consumption (again possibly a
feasibility criteria for use on smaller FOBs due to power budget)
Intrabase network costs are expected to be very high for procurement, as a variety of interconnections and associated hardware components may be
required to link previously disconnected local area FOBs and camp outposts
Concept 3:
Microphone based shot detection systems such as Boomerang will have medium-high up front development costs, as calibrations will be required for
the variety of sonic signatures from different munitions in a range of environments
Radar’s reasonable procurement system cost is somewhat offset by higher operational costs due to very high power consumption (again possibly a
feasibility criteria for use on smaller FOBs due to power budget)
Concept 4:
A dedicated satellite launch is anticipated to be a need in order to support the network of FOB automated base defense systems, which accounts for the
high system element cost assigned
Unmanned Aerial Vehicles, semi autonomous weapons, and unmanned ground vehicles all have relatively high up front development costs and high
operating costs. (Power budgets may also be a concern for the smaller FOBs, where no power infrastructure is available to integrate with.)
In addition UMS have a relatively low reliability and more expensive specialized components for replacement which will ultimately drive up the cost of
the O&S.
Microphone based shot detection systems such as Boomerang will have medium-high up front development costs, as calibrations will be required for
the variety of sonic signatures from different munitions in a range of environments
Sensor types may experience reliability performance shortfalls, as this could mark the first fixed battlefield usage for some, potentially requiring
ruggedization during development or after first deployment and many spares
Notes: Dan – Utilizing the cost estimates and looking at the technologies explain what some of the life cycle cost differences might be (ie higher parts cost due to low reliability, specialized parts etc.) Explain how procurement and development might be cheaper but Total Life Cycle Cost is higher (if that’s the case)

## Slide 6: Value System Weighting Prioritized Stakeholders Assessment of Priority

## Slide 7: Variant Value Score
Notes: Christy – Need to update Highlighted ones

## Slide 8: Variant Value Score

## Slide 9: Value Curves
Chart: Threat Neutralization Value Curve
| 9 | 7 | 5 | 3 | 1
 | 1 | 0.6 | 0.31 | 0.13 | 0
Chart: Classification Accuracy Value Curve
| 9 | 7 | 5 | 3 | 1
 | 1 | 0.76 | 0.41 | 0.13 | 0
Chart: Reliability Value Curve
| 9 | 7 | 5 | 3 | 1
 | 1 | 0.84 | 0.65 | 0.4 | 0
Notes: Getting these!

## Slide 10: OMOE vs Cost Evaluation
Concept | Cost Score | Performance Score
1 | 1.00 | 0.6252
2 | 0.82 | 0.5676
3 | 0.75 | 0.4782
4 | 0.79 | 0.4425
Assessed the performance based on the previously prioritized stakeholders and their importance placed on the individual Evaluation
measures used to determine the value system.
The Evaluation Measures were weighted based upon the importance to the stakeholders and the weighting placed on the individual
stakeholders.
The performance was then normalized.
The cost was determined utilizing a high level assessment of expensive, moderately expensive and affordable (1,2,3 respectively) that was
then summed up and normalized as well.
Those normalized numbers were then graphed against each other
Chart: Cost vs Performance
| 1 | 0.82352941176470584 | 0.75490196078431371 | 0.79411764705882348
 | 0.62515 | 0.56762 | 0.47821 | 0.4425

## Slide 11: Preferred Concept Alternative
Justification:
There is no cost constraint , however we are aware that cost is never a non factor. It was assessed independently and
then utilized to help determine the best ROI for the system.
We took all the data for the OMOE and the cost and we normalized that data. Utilizing a formula to account for the
higher cost we weighted the cost of the system to be a 20% impact to the overall system total. We are also aware that
performance is of great importance to the user because of the nature of the system which will help alleviate adverse
mission impacts and loss of life due to small FOB attacks.
The chosen system has a higher level of risk because it is a semi autonomous system, however it will be progressively
advanced and will meet the requirement of automating lower level functions such as detection, target acquisition,
threat assessment and automated warnings.
The system is slightly more expensive then the other concept options, however we feel this system will be the most
efficient because it will rely heavily on those automated responses and require only the input of the user to make
decisions such as commands to mobilize, command to apprehend or command to engage.
Concept | Detection System | Assessment System | Communication System | Defense System
Semi Autonomous | Passive Infrared Detector Radar Semi Autonomous UMS | Blue Force Tracker Biometric Scanner Computer SW IR/Thermal/NV Imaging Threat Prioritization Matrix SW | Computer Siren Intrabase Network | CROWS Semi Autonomous Armed UGV Deployable Tire Spikes

## Slide 12: SV-7
Summary:
This Systems Measures Matrix shows the eight most crucial metrics for successful mission achievement. Each of the metric includes performance measures to achieve the mission goals. Increment One will be released in FY14 and will drastically increase detection range around the perimeter of the FOB, allowing for a substantially quicker response to threats. Increment Two will be released in FY16 and continues to quicken the response time toward threat. Increment Two accomplishes this by reducing data latency time, time required to warn personnel, and time required to kill threat.
ROBOCOP SV-7 |  |  |  | 
Increment |  | FY12 Baseline | FY14 Inc One | FY16 Inc Two
Increment Purpose |  |  | Increase the detection capability to allow for more stand off time. | Decrease the amount of time needed to communicate, warn, and kill threat.
System |  | Performance Range (Threshold and Objective) Measures |  | 
Detection Package | Detection Range (meters) | (500/1500) | (750/2000) | (750/2000)
 | Location Accuracy (% Correct) | (92/95) | (92/95) | (92/95)
Assessment Package | Identification Accuracy (% Correct) | (92/99) | (92/99) | (92/99)
 | Classification Accuracy (% Correct) | (92/99) | (92/99) | (92/99)
Communication System | Data Latency (milliseconds) | (400/100) | (400/100) | (200/75)
Warning System | Warning Time (seconds) | (3/1) | (3/1) | (2/1)
Weapon System | Kill Time (seconds) | (50/30) | (50/30) | (45/20)
 | Threat Neutralized (% Neutralized) | (95/99) | (95/99) | (95/99)

## Slide 13: SV-9
Explanation:
ROBOCOP SV-9 |  |  | 
IBDS Service | Technology Forecast |  | 
 | Short Term (0-6 Months) | Mid Term (6-18 months) | Long Term ( 18-36 Months)
Detection Devices |  |  | 
RADAR | Blighter B402 | Blighter B422 | Blighter B442
UMS | Tele Operated Talon | Semi Autonomous UMS (ALFUS level 3) | Semi Autonomous UMS (ALFUS level 5)
Assessment Devices |  |  | 
Blue Force Tracker | Blue Force Tracker | Blue Force Tracker 2 | Blue Force Tracker WP
Biometric Scanner | SEEK II | LR SEEK II | Behavioral
Computer | E6400 XFR |  | VICTORY Compliant
Infrared Imaging | Fusion-IR Panther XLR | Extended Range Panther XLR | 
Threat Prioritization Matrix SW | Automated Threat Prioritization SW | Automated Threat Prioritization SW II | 
Communication Systems |  |  | 
Computer | E6400 XFR |  | VICTORY Compliant
Siren | COTS Siren |  | 
Intrabase Network | Wired Fiber Optic LAN |  | VICTORY Compliant LAN
Defense Systems |  |  | 
Semi Autonomous Weapon | CROWS | Slue-to-Cue | Active Protection System
Semi Autonomous Armed UGV | Tele Operated Armed UGV | Semi Autonomous Armed UGV (ALFUS level 3) | Semi Autonomous Armed UGV (ALFUS level 5)
Tire Spikes | Manual |  | Automatic

## Slide 14
System Baseline
Prioritization Subsystem
Automated Threat Prioritization SW
Dissemination of Information Subsystem
E6400 XFR
Wired Fiber Optic LAN
Warning Subsystem
COTS Siren
Data Transportation Subsystem
Wired Fiber Optic LAN
Engagement Subsystem
CROWS
Semi Autonomous Armed UGV
Penetration Prevention Subsystem
Manually Deployable Tire Spikes
System Baseline
Sensing Subsystem
Passive Infrared Detector
Locating Subsystem
Blighter B402
Tracking Subsystem
Tele Operated Talon (UMS)
Identification Subsystem
Blue Force Tracker
SEEK II
Classification Subsystem
SEEK II
E6400 XFR
Determination of Intent Subsystem
E6400 XFR
Determination of Capability Subsystem
E6400 XFR
Fusion-IR Panther XLR
System Baseline

## Slide 15: Summary of Results
Due to the fact that cost was not a major contributing factor is system selection, we determined that the best system for the base defense was the Semi Autonomous Concept.
  This is a high cost, high risk, high reward system. One of the trade offs that was made is that there is a baseline of technologies for the system that will come close to meeting all the requirements. However there is a large opportunity for improvement as far as performance and additional gaps that may be able to be addressed.
  We were able to identify some of the risks involved in the system and had to make decisions based on some of the requirements put forth by the user. For example, the stakeholders identified the need for automated lower level functions, now that carries a greater technical and schedule risk than manual systems. However, we initially may have to trade off the requirement for limited contractors in the field due to the specialty nature of the unmanned systems and the maintenance training required.
    Ultimately the goal would be to transition many of those contractors out and to become a more organic Army, however that will require the specialization and potential MOS of unmanned or robotic systems.
Additionally, we identified that there was a very close system value between the Autonomous Concept and the Video Based Concept, however the Autonomous Concept offered more performance than the video based system, therefore we chose the higher cost system of the two ultimate choices.
There is more analysis to do however, we are confident that with the trade studies we have performed we are ready to recommend the Semi Autonomous Concept and accept the risks involved by implementing mitigation plans to work them.
Notes: Christy

## Slide 16: Appendices
Notes: Elluminate Session to define this

## Slide 17: Appendix A
See Attached Appendix
Notes: Elluminate Session to define this

## Slide 18: Appendix B Test Program Plan (Type 2)
Overview
The ROBOCOP IBDS is designed to protect smaller FOBs from threats such as RPGs, VBIEDs, Hostile Civil Disturbances and small arms fire. The system consists of multiple subsystems that can be individually tested. However, one of the greatest challenges is integration of subsystems. Below is a outline of the Type 2 Testing to be performed.
1) Performance Test
Performance testing will be completed on the following subsystems:
Detection System
  Sensor System
  Radar System
  Tracking System
Assessment System
  Identification System
  Classification System
Communication System
  Warning System
  Data System
Weapon System
  Remote Weapon System
  Penetration Prevention System
Integration and System Level Testing
The final test that will be required will be to ensure that the subsystem can perform without degradation to the mission or individual components when working together. The component level testing can be completed at the contractor facilities, however integration testing and system performance testing will be conducted at a government facility to ensure the conditions remain stable.
2) Environmental Qualification Test
The system will be exposed to a variety of environmental tests that will be dictated by both MIL-STDs and any extreme conditions identified in the mission profile. Therefore the following environmental testing will be conducted:
Temperature Cycling
Shock
Vibration
Humidity
Wind
Dust and Sand
Explosion proofing
Electromagnetic interference
All of the environmental testing will be completed at government facilities.
Notes: Elluminate Session to define this

## Slide 19
3) Structural Tests
The material that will be used in the development of the IBDS will undergo the following structural tests:
Stress
Strain
Fatigue
Bending
Torsion
This testing will be done at the contractor facilities, as it will be conducted on the individual component materials and no on the system as a whole. Some of the subsystem may not require structural tests depending on the material usage. All results will be reported to the government in the form of CDRLs.
4) Reliability Qualification Test
Reliability testing will be conducted at both the subsystem and system level. At the subsystem level this will consist of individual reliabilities since the overall system reliability is defined as:
Rsystem = R1*R2*R3*R4*Rn
It is important to understand the subsystem reliability because it ultimately drives the system level reliability. Component level reliability testing will be done at the contractor facilities. This will also include durability testing to determine Mean Time between Failures (MTBF). The system level reliability testing will be completed at the government facilities. These test results will also provide insight into the Operation Availability which is defined as:
5) Maintainability Demonstration Test
Maintainability Demonstrations will be conducted to demonstrate the mean time to repair (MTTR), both preventative and corrective, as well as if special tools are required. Initially demonstrations can take place at the contractor facility. However, the demonstrations will be conducted at the government facilities as well, with the personnel that will be performing the maintenance. These results will also influence the Operation Availability (see above).
6) Support Equipment Compatibility Test
Support equipment compatibility test will be conducted to ensure compatibility with current handling and transportation equipment, specifically sling load testing for SWAP. These tests will be conducted at the government facilities to ensure the correct equipment and personnel are available.
7) Software Verification
Software Verification will be conducted to ensure software in the following systems is compatible, reliable and performs as required with specified systems:
Intent Determination Software
Capability Level Software
Prioritization Software
Testing can be conducted at the contractor facilities.
AO = –––––––––––––––––––
MTBF
MTBF + MTTR + MLDT

## Slide 20: Top Instantiated Concepts - Review
Concept | Detection System | Assessment System | Communication System | Defense System
1 | Passive Infrared Detector Radar Semi Autonomous UMS | Blue Force Tracker Biometric Scanner Computer RF Detection Threat Prioritization Matrix | Computer Siren Intrabase Network | Semi Autonomous Weapon Semi Autonomous Armed UGV Deployable Tire Spikes
2 | Radar Infrared Camera Camcorder | Blue Force Tracker IR/Thermal/NV Imaging Vector Analysis Video TPM | Siren Intrabase Network Server System | Semi-Autonomous Armed UGV Deployable Tire Spikes
3 | Microphone Boomerang Radar | IR/Thermal/NV Imaging Biometric Scanner Computer Threat Prioritization Matrix | Radio Lights Computer System | Semi-Autonomous Armed UGV Deployable Tire Spikes
4 | Inertia Sensor Microphonic Systems Unmanned Aerial Vehicle (UAV) | Ground Sensor Sonic Signature Computer Response Matrix | Satellite Phone Computer | Semi – Autonomous Weapon Deployable Tire Spikes
Notes: Teram…Elluminate Session to do this

## Slide 21: MOEs, TPMs and KPP Mappings
MOE | TPMs | KPPs
Percentage of Potential threat Detections in the AOR | The IBDS shall detect a 0.3m object in the AOR form 50 to 1500m The IBDS shall detect a XXX mortar or rocket inbound from 5km to 50m | The IBDS shall correctly identify common objects, including common military objects, animal, person, environmental etc, with a 92%(T), 99%(O) accuracy. Rationale: Identification of object within the AOR is key to classification and threat/intent assessment.
Percentage of correctly classified threats | The shall identify Friend, Foe and munitions from 50m to 1500m with a latency of 400ms(T), 100ms(O) | The IBDS shall correctly classify the potential threat as friend, foe, munition or neutral with an accuracy of 95%(T), 99%(O). Rationale: Correct classification including threat/intent is critical to providing an early warning to personnel and QRF.
Percentage of Personnel cleared of danger area and ready for mobilization | The IBDS shall output an audible warning automatically within 3s(T), 1s(O) of the recognition of an incoming munition. | The IBDS shall provide 30s warning to Base personnel and QRF in response to incoming threat based on flight time of XXX Mortar round at XXX distance (See Classified Annex). Rationale: With appropriate detection a 30s warning to scramble the QRF and to clear base personnel will reduce the number of casualties.
Percentage of threats neutralized without damage to the personnel, facilities or equipment | The IBDS shall render a threat neutral (unable to cause damage) within 50s(T), 30s(O) of recognition of the potential threat. | The IBDS shall render 95%(T), 99%(O) of the incoming munitions neutralized. Rationale: Neutralization of the incoming munitions/attacking forces will prevent/reduce damage to base infrastructure and personnel as well as acting as a deterrent to future attacks.
Availability of .9 | The IBDS shall have an Operational Availability of 0.90 | The IBDS shall be operationally available 90% (T) 92% (O) of the time
Mean time between failures of 750 hours | The IBDS shall have an MTBF of 750 hours | The system shall have a reliability of 750 (T) 1000 (O) hours mean time between failures
Notes: Bill Berklich