## Slide 1: Project 2
Group 4
Douglas Brown
Jessica Hale
Steve Mazza
Daniel Torres
Notes: Introduce yourself.
Introduce your team.

## Slide 2: The Problem
Threat
Incoming targets
Mean time of arrival: 3 minutes
Defense
Rail gun
Mean cycle time: 1.5 minutes
Analysis
Queue & Service model
Differentiable from Car Wash model
Notes: Time: 2 minutes
Threat:
Incoming targets are assumed to arrive on average every 3 minutes with an exponential distribution.
Defense:
A rail gun is under consideration for use in providing fire support to expeditionary forces. Utilization of a rail gun is of interest because it has the potential to improve on the capabilities exhibited by currently used large artillery batteries. Rail gun systems have potential to extend the strike range from approximately 15 miles for current artillery to up to 250 miles while using projectiles that are lighter weight and have better handling and transport characteristics. Because a rail gun has a high velocity projectile, it is estimated it could hit vehicles, buildings, assembled enemy combatants, and other key targets at distances up to 250 miles away within 5 to 7 minutes of a round being fired. It is clear that a rail gun system could provide a potential leap forward capability to the military.
Analysis:
A key factor to consider is that this is not a typical simple discrete event simulation of a car wash or sandwich shop. In those simulations, it is beneficial to keep the server busy and not pay for idle time. There is a balance or tradeoff between the acceptable queue time and server utilization. In our case, I suspect the user would indicate a quick response to a call for fire support trumps keeping the rail gun crew busy.

## Slide 3: The Model
Targets
Queue
Rail Gun
Notes: Time: 2 minutes
Description:
A discrete event ExtendSim model was developed for a single rail gun system. Discuss the process from target arrival, queuing, and engagement.
Assumptions:
Exponential distributions were utilized for all arrival and server (rail gun) times. The model consists of a target being identified with a request for fire support being identified, the call for fire support entering a queue, and the rail gun system being prepared, charged, and firing at the target. In this model, the probability of kill is considered to be 100% for each round fired. The additional blocks in the model provide a means to graphically review simulation results, input information to the model, or collect data from the model.

## Slide 4: The Results
Initial insight
Is a single rail gun sufficient?
What is the impact of delay?
What is the effect of reduced interarrival time?
Model variations and improvements
Capturing success and failure
Number of guns vs. cycle time
Normal vs. exponential distribution
Notes: Time: 4 minutes
Initial insight:
Is 1 gun enough: This input is based strictly on the utilization data collected earlier. In most cases a lower utilization will mean less queuing for customers but will mean that the system is idle more (which could be considered inefficient). In production, an increase of utilization will require more preventative maintenance and more wear and tear on the machine. Using the data collected I found that gun utilization is ~ 33% (please someone double check my math?). With that, I feel like there is room for improvement so I would conclude that there is not enough guns on hand.
The average maximum wait for the 30 simulation runs in the queue was 10.21 minutes, with one run exhibiting a 15 minute queue delay. The average max delay per run at the rail gun was 8.47 minutes, with the high being over 11 minutes. If we assume a 5 minute in air time for the rail gun projectile to reach targets, it ends up being a question of whether the user will tolerate situations each day where more than 15 minutes is required between the call for fire support and the target being eliminated. This assumes a 100% elimination rate per fire.
Dan: you can answer this best.
Model variations and improvements:
An improvement to our discrete event ExtendSim model was developed (see Figure X) for a single rail gun system. Exponential distributions were utilized for all arrival and server (rail gun) times. In this model, the probability of kill is considered to be 100% for each round fired. Results indicate 50.6% of the overall time until a target is fired upon is caused by queue delays. Queue delays are due to the single rail gun being occupied with actions required to fire at earlier target requests. An improvement to our discrete event ExtendSim model was developed (see Figure X) for a single rail gun system. Exponential distributions were utilized for all arrival and server (rail gun) times. In this model, the probability of kill is considered to be 100% for each round fired.
We looked at a number of metrics for distinguishing two conditions, one where we have a single rail gun with a mean cycle time of 1.5 minutes and another where we have four rail guns each of whose cycle times are six minutes. When we approached this analysis we assumed that minimizing queue length would be tantamount to maximizing target acquisition and, hence, would indicate an increase in the likelihood of successful kills on the battlefield. What we found, however, was that the queue length in both models is relatively short and an analysis of variance (1-way ANOVA) indicates no statistical difference in this metric. So we looked at other indicators such as average length, average wait, max length, max weight and utilization. All of these have p−values less than α which supports unequal means in these data. The average and maximum wait times are shorter with four rail guns than with one and the data is statistically significant. Focusing on these criteria, we infer that four guns would result in a faster acquisition and kill time and therefore pose significantly less risk to material damage and human life.
The time between call for fire support was changed from an exponential distribution to a normal distribution with mean of 3.0 minutes and standard deviation of .25 minutes. The gun cycle time was altered from an exponential distribution to a normal distribution with mean of 1.5 minutes and standard deviation of .5 minutes. The modifications resulted in a drastic change in the behavior of the rail gun model, with any queue waiting times being virtually eliminated. Using 30 simulation runs, the average time until a target is fired upon drops from 2.800 minutes with the exponential distribution to 1.499 minutes with a 90% CI of (1.488, 1.511) for the normal distribution. The average wait in the queue dropped from 1.310 minutes with the exponential distribution to .0009 minutes for the normal. The fractional average of the time until a target is fired upon that is due to queuing delays dropped from 46% to .058% for the normal distribution. A graphical investigation of plots for targets killed, queue length, rail gun delay, and queue wait time did not reveal a transient state within the normally distributed model. The standard deviation of the normal distributions plays a critical role in the change in results, as it indicates how widely the time values will vary from the mean. As we know, 3 standard deviations from the mean will account for 99.7% of the values. The small standard deviation of .25 minutes for targets generating a fire request feeds the model in a smoother fashion than the exponential distribution. Even with a larger standard deviation of .5 at the rail gun, the model has no problem quickly responding to calls to provide fire support. In 30 runs, the average maximum wait in the queue was .12 minutes, as opposed to 10.22 minutes in the exponential distributions. The exponential distribution is commonly used for waiting time, failure rates, or events where the rate of occurrence remains constant over time. It is important to consider that an exponential distribution has a memoryless property that a normal distribution does not have. This means that the probability of an event occurring at any point in time is the same and independent or not influenced by how long the current wait has been. This feature of exponential distributions contributed to the delays exhibited in the exponential distribution rail gun model.

## Slide 5: Conclusions
Average and maximum wait times
Equipment failure rate (MTBF)
Weapon effectiveness
Notes: Time: 2 minutes
Ramble for 2 minutes or the balance of time you’ve got. If you need to kill time, feel free to re-hash all of the metrics and statistics from the previous slide. Say things like, “Like I stated earlier…”